Engine Fire Panel

# Text boxes

## FUEL SWITCHES

-Illuminates red when respective fire handle illuminates

-Remains illuminated if the fire warning still exists

-With the Fire Handle pulled and the fire warning

terminated, this light stays illuminated until it is moved

to OFF

AGT  LOW (1 or 2) light

Illuminates when respective bottle is discharged (battery bus powered)

Memory Item

Engine Fire – Throttle Idle

# ENGINE FIRE HANDLES

-Illuminates for an overheat or fire in the respective engine nacelle

-Remains illuminated until the fire / overheat no longer exists

-Simultaneously to fire handle illumination, the following occurs:

-Fuel switch illuminates red for the respective engine

-Master warning light illuminates

-EAD annunciation

-Fire bell sounds

Pulling the fire handle accomplishes the following:

-Silences alarm (if not silenced by pressing the master wrng switch)

-Disconnects the generator field

-Closes the Hyd Fire Shutoff Valve

-Closes the Fuel Fire Shutoff Valve

-Shuts down the associated Air System (if Air Sys in Auto mode)

Rotating the Fire Handle (after pulling)

-Discharges the respective agent bottle into the engine nacelle