### FINAL COCKPIT PREPARATION

Captain					First Officer

Parking brake 	Set		OPS Computer		complete

Fuel Quantity		Chk		Flap T/O Selector	sET

FMS (final pages)	Load		Flt Ctrl Panel	SET

IRS			CHECK

##### Captain/PF

TAKEOFF BRIEFING	COMPLETE

(Initial portion of briefing)

BEFORE START CHECKLIST		ENTRY DOORS		SECURE

### WHEN CLEARED TO START

Captain	 				First Officer

ENGINE IGNITION 	A or B		BCN 				ON

AUX HYD PUMP 1 		ON

BELOW THE LINE					(Fuel, Air Panel -Manual)

## AFTER START PROCEDURE

Captain 				First Officer

TRIM 	   __UNITS, ZERO ZERO		ANTI-ICE 			AS REQUIRED

APU 				OFF

AFTER START CHECKLIST			AUTOBRAKE			T.O.

(Air, Hyd Panel -Manual)

### BEFORE TAKEOFF PROCEDURE

#### Captain					First Officer

SPOILERS 		ARMED 	FLAPS/SLATS			SET

#### Select PROF (and Nav, if applicable) and set 121.5 in VHF radio number 2

FLIGHT CONTROLS 	CHECKED 	FLIGHT CONTROLS		CHECKED

EAD 			CHECKED	(Hyd, Air Panel -Manual)

EAD 				CHECKED

##### PF

TAKEOFF BRIEFING	COMPLETE

(Operational procedures portion of briefing)

BEFORE TAKEOFF CHECKLIST

WHEN CLEARED FOR TAKEOFF

##### Captain					First Officer

EXTERIOR LIGHTS	SET		RADAR				ON

TRANSPONDER		ON

AFTER TAKEOFF PROCEDURE

PF					PNF

SPOILERS 			DISARMED

AUTOBRAKE 			OFF

FLAP T.O. SEL THUMBWHEEL 	15°

AFTER TAKEOFF CHECKLIST 		(Air, Hyd, Fuel System -Manual)

AFTER LANDING PROCEDURE

F/O contacts GRND CTL for clearance before the After- Landing procedures are accomplished

Captain					First Officer

GROUND SPOILERS	DISARMED 	TRANSPONDER 		AS REQUIRED

EXTERIOR LIGHTS 	SET		RADAR				OFF

# FLAPS/SLATS 			UP/RET

AUTOBRAKE 			OFF

STAB TRIM			SET 3O ANU

ANTI-ICE 			AS REQUIRED

APU 				AS REQUIRED

ENGINE FUEL SWITCH		AS DESIRED

(After 3 mins)

SHUTDOWN PROCEDURE

Captain					First Officer

PARK BRAKE		AS REQ’D	TRANSPONDER		OFF

ELECTRICAL POWER	AS REQ’D	BEACON			OFF

FUEL SWITCHES	OFF		SEAT BELT SIGN		OFF

SD STATUS PAGE	CHECK		ANTI-ICE			OFF

(Hyd, Fuel System -Manual)

SHUTDOWN CHECKLIST			EMERGENCY POWER SWITCH	OFF

SD STATUS PAGE		CHECK

SECURE PROCEDURE

Captain					First Officer

PARK BRAKE		RELEASED	EMER LIGHT SWITCH		OFF

LOGBOOK		COMPLETE	IRS				OFF

APU/EXT PWR			AS REQUIRED

SECURE CHECKLIST			BATTERY SWITCH		AS REQUIRED

OPS COMPUTER		OFF

VOICE RECORDER CB		AS REQUIRED