# MD-11 Limitations

Max Taxi Weight - Center Gear Extended			633,000

Max Takeoff Weight - Ctr Gear Extended			630,500

Max Landing Weight - Ctr Gear Extended			491,500

Max Autoland weight – Ctr Gear Extended			491,500

Max Zero Fuel Weight - Ctr Gear Extended			461,300

Maximum Runway Slope					+/- 2%

Max Tailwind - T/O or Landing				10 kts

Non-precision appchs                      A/P off no later than 50 ft below MDA

Max lateral fuel imbalance between 1 & 3			2,500

GE - Max start EGT  (No time limit)			750

GE - Max start EGT  (40 seconds)				750-870

PW - Max start EGT  					535

PW - Max start EGT  (Flight)				650

MD-11 Memory Items

All Engine Flameout	Eng Ign Ovrd Switch - Ovrd On

ADG – Deploy

Tailpipe Fire		Fuel Switch - Off

## Engine Abnormal Start	Fuel Switch - Off

(Hot, Hung, or No Start)

Two Engines Inoperative	Throttle – MCT

Flaps (unless on final) – Up

Speed (unless on final) - Drftdn or up/ret Vmin+30

Gear (unless committed) – Up

Slats (unless on final) – Ret

Cabin Altitude		Oxygen Masks – On/100%

Outflow Valve - Verify closed

Cargo Fire Lower		Flashing Cargo Fire Agent Disch Switch – Push

Eng 2 A/I Duct		Engine 2 throttle – Idle

Engine Fire 		Throttle – Idle

(or Severe Damage)

Airspeed: Unreliable	AFS OVRD and FD Switches – Off

Aircraft Pitch/Thrust

- Flaps and/or Slats Extended – 10o and 90% N1

- Flaps and Slats up - 4o and 90% N1