# Pressurization Panel

# Text boxes

SYSTEM – SELECT / MANUAL Switch

Allows selection between MANUAL and AUTO

Two alternating auto channels (1 primary, 1 stby)

SELECT (illuminated)

-Both (auto) control channels failed. System has automatically

switched to manual mode.

MANUAL (pressed and illuminated)

- System locked in Manual mode.

- Pressing a second time selects other auto channel.

Outflow valve indicator

Displays outflow valve position (in Auto or Manual mode)

MANUAL LDG ALT

-Used to enter landing field elevation if not available from FMS database.

-Inhibited with CABIN PRESS switch in MANUAL mode.

-Knob must be turned 120o to operate.

-Value is shown on Air Synoptic (boxed).

## DITCHING Switch

Controls the rate of depressurization, and seals any ports associated with the Air System that would allow entry of water after ditching

ON (Pressed and illuminated)

-Maintains existing cabin altitude

during descent

-At 2500 ft or <.5 PSID (whichever 1st)

-Packs and bleeds shut off

-GPWS is inhibited

-Avionics venturi closes (in auto mode)

-Outflow valve opens (in auto mode)

-Ram Air Doors close

-At 1000 ft

-Outflow valve closes.

When slats are extended for T/O, cabin is pressurized to 100 ft below departure airport field elevation.  Cabin will return to departure airport field elevation if aircraft descends before reaching 5,000 ft.

##### Memory Item

#### Cabin Altitude

### Oxygen Masks - On/100%

Outflow Valve – Verify Clsd

###### CLIMB – DESC

Allows manual selection of outflow valve position in manual mode

CLOSED (illuminated)

Indicates that the outflow valve is fully closed